# OSDP Test VM Operating Guide

24 Jan 2016 Rodney Thayer rodney@smithee.us

### Overview
- it's a 64-bit debian 7 vm.
- it's shipped as an ova file, exported from virtualbox
- it's set up to just run. You don't need to operate it. It was meant to be useful to share as a fixed-function VM e.g. useful for any dev team, linux or not.
## Installation
### TLS configuration
- fixed certs used, files shipped on the vm. test root included.
- uses gnutls latest configuration, supports TLS 1.2, AES-128-GCM
- configured with default pre-shared interim key from libosdp github repo
### OSDP configuration
assumes pd is at address 0.
no secure channel (secured instead by TLS.)
### vm set-up
ip address 10.2.0.200
gateway 10.0.0.1
dns: none
login: user osdp, password osdp.
  You have sudo. Root password is also osdp.

1. make sure virtualbox is running on your host platform
2. import the vm
3. make sure the vm's first ethernet interface is bridged to a real ethernet
4. start the vm
5. ping 10.2.0.200 from elsewhere on the network to confirm connectivity. It does respond to ping. Note: it's got ports 22,80 and 10443 open if you nmap scan it.
### vm operation
- use a browser to access http://10.0.0.200/open-osdp-CP.html. There is a primitive html/cgi-based UI on an apache web server on port 80. No authentication, this is an un-insulated engineering testbed.
- the "display status" link will spawn a second page with current CP status
## Demonstration
- start the vm
- ping it to confirm it's alive
- go to the web UI
- start the status page
- from a PD, connect to the CP.
- console access can show the incoming connection
- use network trace tool to show the TLS traffic
- from the PD, present a badge (raw format, 26 bit)
- observe the status change on the CP status web page.
- console access can show the diagnostic log
### Contents
- ova file
- /home/osdp is where everything is built
- setup directory is necessary extras
- includes open source
- includes platform set-up (apache config, etc.)
- libosdp-1.0build4 is sources
- runs out of /opt/open-osdp/run/CP
- started at boot time from /etc/rc.local (calls file /opt/open-osdp/bin/up.osdp)
- uses open source components: gnutls, nettle, libtasn, jansson