Osdp conformance tester

# Appendix
## A. Colophon
part of libosdp-conformance, see github.com/security-industry-association/libosd-conformance.

## B. Integration with Linux

The programs all run out of /opt/osdp-conformance. There are programs and shell scripts in bin, cgi programs and shell scripts in cgi-bin, and web UI contant in www. In my environment I drop all the cgi-bin files into my normal cgi-bin and all the www files into my web server root and just run with it.

This makes the shell scripts and programs run as the apache httpd user. I add a file to /etc/sudoers.d so that “sudo -n” works in the shell scripts. Note this is an un-insulated implementation meant for use in a laboratory.

Sample files are in doc/linux-devuan-samples

## C. Commands
These are the values allowed for the “command” field in a command json file. These are from oo_cmdbreech.c

conform_2_6_1
text
message=<string to send>
capabilities
dump_status
identify
initiate_secure_channel
input_status
local_status
led
perm_on_color …
output
present_card
reader_status
reset_power
send_poll

slow_timer – set to 1 to implement timer acceleration for TLS case. If anything comes in (like a gratuitous noise byte) this means you shoujld send a poll.

tamper