libosdp-conformance guide

Note: interim document, contains merges from previous documents. Might be transiently incoherent.

# Use
## Operation
Build the linux source. From your web browser access open-osdp-CP.html. “start” the program. From an ssh console tail /opt/osdp-conformance/run/CP/stderr to confirm it started. The log is in /opt/osdp-conformance/run/CP/open-osdp.log.

You can do all of this from the command line if you want. Note since it access the serial port it needs to be run as root (typically with sudo.)

### settings and saved configuration
t.b.d.
## Logs and Traces
A log is created fresh each time the program is started. The filename is osdp.log, it is created in the directory where the program is started.

A trace can be created. The trace command toggles tracing on and off. The trace is written to the file current.osdpcap in the directory where the program is started. See the appendix for a description of the trace file format.
## Commands
These are the values allowed for the “command” field in a command json file. Some commands take sub-options (some are mandatory, some are optional.)
### acurxsize
[ACU]
Sends osdp_ACURXSIZE to PD, using value from the code (approx 1k.)
### bio_read
### busy
busy
Causes the PD to respond with BUSY to next incoming command.
### buzz
[ACU]
buzz [off_time=xx] [on_time=xx] [repeat=xx]
default
15 15 3
### capabilities
[ACU]
capabilities - sends an osdp_CAP to the PD.
### comset
[ACU]
comset [new_address=xx] [new_speed=xxx]
Sends a command to request to set the speed and address of the PD. New_address must be 00-7E (hex.) new_speed must be a valid sped (9600,115200,etc.)
### conform_x_x_x
[ACU PD]
These are used to induce various conditions for conformance testing. The numbering comes from the old profile documents section headings.

conform_2_2_1
conform_2_2_2
conform_2_2_3
conform_2_2_4
conform_2_6_1
conform_2_11_3
conform_2_14_3
conform_3_14_2
conform_3_20_1
### dump_status
### factory-default
[ACU PD]
factory-default
removes saved parameters settings (i.e. the preshared key.)
### genauth
[ACU]
genauth [template=<witness | challenge>] [algoref=<algo>] [payload=zzz]

Template is the challenge operation type (witness crypto or challenge cryto)
algoref is the algorithm used.
payload is the value to be sent as the input payload.

<algo> must be the character strings 07 or 11 or 14 (rsa, ECC P-256, ECC P-384)
### identify
[ACU]
identify - sends an osdp_ID to the PD.
### induce-NAK
[PD]
induce-NAK - causes the PD to NAK the next incoming message.
### initiate-secure-channel
[ACU]
initiate-secure-channel [key-slot=x]
Initiate a secure channel session by sending an osdp_CHLNG. Key slot specifies the key to use, 0=SCBK-D, 1=the preshared key.
### input_status
[ACU]
local_status - send osdp_LSTAT request.
### keep-active
keep-active [milliseconds=xx]
Sends osdp_KEEPACTIVE. Default value is 7000 (7 milliseconds.)
### keypad
keypad [digits=zzz]
Sends a key input or the (1-9) digits specified. Value for the digits option is 1-9 OSDP keypad values (0-9,*,#)
### keyset
[ACU]
keyset [psk-hex=zzzz]
sends an osdp_KEYSET. Default is to send the key specified in the settings. the psk-hex option provides a hex value for the key. Key must be 16 octets (so 32 hexits.)
### led
[ACU]
led [led-number=x] [perm-control=x] [perm-off-time=x] [perm-off-color=x] [perm-on-time=x] [perm-on-color=x] [temp-off-color=x] [temp-off=x] [temp-on-color=x] [temp-timer=x] [temp-control=x]

default
LED 0
control=set
off-time=0
off-color black
on-color green
on timer 30
reader 0
temp - no operation
### local_status
[ACU]
local_status - send osdp_LSTAT request.
### mfg
[ACU]
mfg [command-id=xx] [command-specific-data=aaaa] [oui=aabbcc]

command-id is in decimal.
command-specific-data is the payload.
oui is the organizational unit identifier.
### operator_confirm
[ACU PD]
operator_confirm test=xxx
confirms test xxx ran successfully.
### output
[ACU]
output - outputs via osdp_OUT. The default is output 0, permanent on immediate, forever.

output [output-number=x] [control-code=x] [timer=x]
### output_status
[PD]
send osdp_OSTAT to the PD.
### polling
[ACU]
polling enables or disables sending poll commands.
"polling" toggles the setting.

"polling action=reset" resumes polling and resets the sequence number to 0.

"polling action=resume" just resumes polling.
### present_card
[PD]
present_card [raw=xxx] [bits=n] [format=p-data-p]
sends an osdp_RAW to the ACU.

Options:
"bits" sets the bits in the message to the specified value.
- "format" sets the format to raw, "format=p-data-p" sets the data to P-data-P.
- "raw" sets the card value to the specified hex string. string must contain enough hex bytes to contain the specified number of bits.
### reader_status
[ACU]
reader_status - send osdp_RSTAT to PD
### reset
[ACU]
reset - resets sequence number to 0
### reset_power
[PD]
reset_power - induces a power reset condition (reset after nex time LSTATR is sent.)
### send_poll
[ACU]
send_poll - directs the ACU to send a poll.
### stop
[ACU MON PD]
stop - directs the program to stop.
### tamper
[PD]
tamper - induces a tamper condition (reset after next time LSTATR is sent.)
### text
[ACU]
text message=zzz sends message in osdp_TEXT.
### trace
[ACU PD MON]
toggles tracing of OSDP data to ./current.osdpcap.
### transfer
[ACU]
transfer [file=fff] - initiates a file transfer. the file zzz is used if no file is specified.
### verbosity
[ACU MON PD]
verbosity [level=x] - set message verbosity. By convention this is 0 (none), 3 (normal), or 9 (debug).
### xwrite
[ACU]

  xwrite [action : get-mode | scan | set-mode | set-zero | done] [apdu : <hex value>]

issues an osdp_XWRITE. The action is get mode, scan, set mode, set zero, or done. an optional apdu hex payload may be provided. Experimental.

## Tools
### Packet Dump
A cgi for packet decode is provided. opt/osdp-conformance/cgi-bin/osdp-decode takes a single field which is a hex string dump (spaces ok.) A command line tool (osdp-dump) is also available.

A command line tool for calculating secure channel values is provided (osdp-sc-calc.)
# Installation
## Building and Installing
### Installing on Devuan
linux-devuan-samples
etc/sudoers.d/www-user
### Integration with Linux
The programs all run out of /opt/osdp-conformance. There are programs and shell scripts in bin, cgi programs and shell scripts in cgi-bin, and web UI contant in www. In my environment I drop all the cgi-bin files into my normal cgi-bin and all the www files into my web server root and just run with it.

This makes the shell scripts and programs run as the apache httpd user. I add a file to /etc/sudoers.d so that “sudo -n” works in the shell scripts. Note this is an un-insulated implementation meant for use in a laboratory.

Sample files are in doc/linux-devuan-samples
Build Instructions for libosdp-conformance

This assumes you are building in a Debian/Ubuntu/Devuan environment but it
should look like fairly normal Linux tools.

This uses the AES implementation at https://github.com/kokke/tiny-AES-c. (An arbitrary decision, other AES implementations could be substituted.)

Set-up:
- performed standard debian update and package set-up
  apt-get update
  apt-get upgrade
  apt-get install build-essential
  apt-get install clang lzip pkg-config libgmp3-dev libgmpxx4ldbl screen
  apt-get install tcpdump gdb apache2 git

- install the dev package for jansson

- NOTE the default make file does not build TLS.
  for TLS, install the dev package for libtasn, nettle, and gnutls.
  gnutls' package installer will pull in libtasn and nettle if needed.

## Build
assumes you are user "osdp" when you do this, and have "sudo".
assumes you do this in /opt/osdp-conformance/setup/libosdp-conformance.
### First set up directories for build...

  sudo mkdir -p /opt/osdp-conformance/setup
  sudo chown -R osdp:osdp /opt/osdp-conformance

Then get and build AES...

### (to build AES code needed for libosdp-conformance)

  cd /opt/osdp-conformance/setup
  git clone https://github.com/kokke/tiny-AES-c
  cd tiny-AES-c
  make
  sudo mkdir -p /opt/osdp-conformance/include
  sudo mkdir -p /opt/osdp-conformance/lib
  cp aes.o /opt/osdp-conformance/lib
  cp aes.h /opt/osdp-conformance/include

### (to build libosdp-conformance)

  cd /opt/osdp-conformance/setup
  git clone https://github.com/security-industry-association/libosdp-conformance
  cd libosdp-conformance
  make clean
  make release
  cd /
  tar xzvf
    /opt/osdp-conformance/setup/libosdp-conformance/release-osdp-conformance.tgz
  ...copy /opt/osdp-conformance/cgi-bin to your cgi-bin directory if necessary
  ...copy /opt/osdp-conformance/www to your www directory if necessary

### Installation:

(to run as CP)

    cd /opt/osdp-conformance/run/CP
    cp open-osdp-params-CP.json open-osdp-params.json
    ... set baud rate and PD address, other parameters

At this point the web UI should work at http://tester/osdp-conforamance-CP.html.
Logs are being placed in /opt/osdp-conformance/run/CP and /opt/osdp-conformance/log.

# Internals
These are from oo_cmdbreech.c

# Appendix
## Standards Conformance
### iec migration
external messages have been converted to say ACU instead of CP.
internal labels still say CP in many cases.

## OSDPCAP Format
This is a "JSONL" format, i.e. each line of text is a whole JSON data object. The fields in the JSON are:
time - time in (see code) format
io - direction - in, out, or monitor
data - data in hex, with intermixed white space, including the marker byte (0xff)
tbd1
tbd2

Example:
{"time":"1570066876.309707865", "io":"out", "data":" ff 53 00 08 00 05 60 da 99"}
# punchlist

card data
examples
command-samples
ACU-actions
config-samples
file default for transfer
clean up output control codes
tests for operator_confirm
default for keypad?
dump_status
various conformance tests