OSDP conformance tester

# Run-Book
conformance runbook for 0.0 build 5

set up as the CP
set up the DUT as the PD
configure the DUT e.g. for address 0, 9600 bps
start the CP
check status to make sure it's run at least 8 packets each way
shell in
cd to /opt/osdp-conformance/run/CP
run the script:
  sudo /opt/osdp-conformance/bin/100-test-all
retrieve the report from /opt/osdp-conformance/log/report.txt or the dated files the
  script places in the current directory.

check the "stderr" log file and open-osdp.log for anomalies and to conform behavior.

# Operation
Build the linux source. From your web browser access open-osdp-CP.html. “start” the program. From an ssh console tail /opt/osdp-conformance/run/CP/stderr to confirm it started. The log is in /opt/osdp-conformance/run/CP/open-osdp.log.

You can do all of this from the command line if you want. Note since it access the serial port it needs to be run as root (typically with sudo.)
# Appendix
## A. Colophon
part of libosdp-conformance, see github.com/security-industry-association/libosd-conformance.

## B. Integration with Linux

The programs all run out of /opt/osdp-conformance. There are programs and shell scripts in bin, cgi programs and shell scripts in cgi-bin, and web UI contant in www. In my environment I drop all the cgi-bin files into my normal cgi-bin and all the www files into my web server root and just run with it.

This makes the shell scripts and programs run as the apache httpd user. I add a file to /etc/sudoers.d so that “sudo -n” works in the shell scripts. Note this is an un-insulated implementation meant for use in a laboratory.

Sample files are in doc/linux-devuan-samples

## C. Commands
These are the values allowed for the “command” field in a command json file. These are from oo_cmdbreech.c

conform_2_6_1
text
message=<string to send>
capabilities
dump_status
identify
initiate_secure_channel
input_status
local_status
led
perm_on_color …
output
present_card
reader_status
reset_power
send_poll

slow_timer – set to 1 to implement timer acceleration for TLS case. If anything comes in (like a gratuitous noise byte) this means you shoujld send a poll.

tamper