Errata: referering to the IEC 60839-11-5 draft as submitted to the IEC as of 21Feb2020

1. Table 56 Page 42 (in 7.12, osdp_KEYPAD.) Third item in "Data" packet format field should read "Keypad data represented as ASCII characters."
2. Annex D section D.7. Only SCBK-D or a pre-set SCBK should be used. Do not use MK, it is unsafe due to it's use of unauthenticated PD input to generate the key.
3. Annex B Function Code Definitions List, item B.10 Function Code 9 -- Communications Security. Should say "Number of: This field is encoded to represent the key exchange capabilities: 0x01 - (Bit-0) default AES128 key, as defined in Annex D. (Bits 7-1) reserved for future use." Also, Compliance levels should remove 0x02 reference and add "(Bits 7-1) reserved for future use".

Errata: referering to IEC FDIS 60839-11-5 draft as 15Apr2020

4. Annex B Function Code Definitions List, item B.17, compliance level 1, should read "60839".
5. 6.12 osdp_TEXT, 6th paragraph should read "Refer to Table 20."

revised 20200422