libosdp-conformance guide

# Use

### settings and saved configuration

## Commands
These are the values allowed for the “command” field in a command json file. Some commands take sub-options (some are mandatory, some are optional.)
### acurxsize
[ACU]
Sends osdp_ACURXSIZE to PD, using value from the code (approx 1k.)
### bio_read
### busy
busy
Causes the PD to respond with BUSY to next incoming command.
### buzz
[ACU]
buzz [off_time=xx] [on_time=xx] [repeat=xx]
default
15 15 3
### capabilities
[ACU]
capabilities - sends an osdp_CAP to the PD.
### comset
[ACU]
comset [new_address=xx] [new_speed=xxx]
Sends a command to request to set the speed and address of the PD. New_address must be 00-7E (hex.) new_speed must be a valid sped (9600,115200,etc.)
### conform_x_x_x
[ACU PD]
These are used to induce various conditions for conformance testing. The numbering comes from the old profile documents section headings.

conform_2_2_1
conform_2_2_2
conform_2_2_3
conform_2_2_4
conform_2_6_1
conform_2_11_3
conform_2_14_3
conform_3_14_2
conform_3_20_1
### dump_status
### factory-default
[ACU PD]
factory-default
removes saved parameters settings (i.e. the preshared key.)
### genauth
[ACU]
genauth [template=<witness | challenge>] [algoref=<algo>] [payload=zzz]

Template is the challenge operation type (witness crypto or challenge cryto)
algoref is the algorithm used.
payload is the value to be sent as the input payload.

<algo> must be the character strings 07 or 11 or 14 (rsa, ECC P-256, ECC P-384)
### identify
[ACU]
identify - sends an osdp_ID to the PD.
### induce-NAK
[PD]
induce-NAK - causes the PD to NAK the next incoming message.
### initiate-secure-channel
[ACU]
initiate-secure-channel [key-slot=x]
Initiate a secure channel session by sending an osdp_CHLNG. Key slot specifies the key to use, 0=SCBK-D, 1=the preshared key.
### input_status
[ACU]
local_status - send osdp_LSTAT request.
### keep-active
keep-active [milliseconds=xx]
Sends osdp_KEEPACTIVE. Default value is 7000 (7 milliseconds.)
### keypad
keypad [digits=zzz]
Sends a key input or the (1-9) digits specified. Value for the digits option is 1-9 OSDP keypad values (0-9,*,#)
### keyset
[ACU]
keyset [psk-hex=zzzz]
sends an osdp_KEYSET. Default is to send the key specified in the settings. the psk-hex option provides a hex value for the key. Key must be 16 octets (so 32 hexits.)
### led
[ACU]
led [led-number=x] [perm-control=x] [perm-off-time=x] [perm-off-color=x] [perm-on-time=x] [perm-on-color=x] [temp-off-color=x] [temp-off=x] [temp-on-color=x] [temp-timer=x] [temp-control=x]

default
LED 0
control=set
off-time=0
off-color black
on-color green
on timer 30
reader 0
temp - no operation
### local_status
[ACU]
local_status - send osdp_LSTAT request.
### mfg
[ACU]
mfg [command-id=xx] [command-specific-data=aaaa] [oui=aabbcc]

command-id is in decimal.
command-specific-data is the payload.
oui is the organizational unit identifier.
### operator_confirm
[ACU PD]
operator_confirm test=xxx
confirms test xxx ran successfully.
### output
[ACU]
output - outputs via osdp_OUT. The default is output 0, permanent on immediate, forever.

output [output-number=x] [control-code=x] [timer=x]
### output_status
[PD]
send osdp_OSTAT to the PD.
### polling
[ACU]
polling enables or disables sending poll commands.
"polling" toggles the setting.

"polling action=reset" resumes polling and resets the sequence number to 0.

"polling action=resume" just resumes polling.
### present_card
[PD]
present_card [raw=xxx] [bits=n] [format=p-data-p]
sends an osdp_RAW to the ACU.

Options:
"bits" sets the bits in the message to the specified value.
- "format" sets the format to raw, "format=p-data-p" sets the data to P-data-P.
- "raw" sets the card value to the specified hex string. string must contain enough hex bytes to contain the specified number of bits.
### reader_status
[ACU]
reader_status - send osdp_RSTAT to PD
### reset
[ACU]
reset - resets sequence number to 0
### reset_power
[PD]
reset_power - induces a power reset condition (reset after nex time LSTATR is sent.)
### send_poll
[ACU]
send_poll - directs the ACU to send a poll.
### stop
[ACU MON PD]
stop - directs the program to stop.
### tamper
[PD]
tamper - induces a tamper condition (reset after next time LSTATR is sent.)
### text
[ACU]
text message=zzz sends message in osdp_TEXT.
### trace
[ACU PD MON]
toggles tracing of OSDP data to ./current.osdpcap.
### transfer
[ACU]
transfer [file=fff] - initiates a file transfer. the file zzz is used if no file is specified.
### verbosity
[ACU MON PD]
verbosity [level=x] - set message verbosity. By convention this is 0 (none), 3 (normal), or 9 (debug).
### xwrite
[ACU]

  xwrite [action : get-mode | scan | set-mode | set-zero | done] [apdu : <hex value>]

issues an osdp_XWRITE. The action is get mode, scan, set mode, set zero, or done. an optional apdu hex payload may be provided. Experimental.

## Tools
### Packet Dump
A cgi for packet decode is provided. opt/osdp-conformance/cgi-bin/osdp-decode takes a single field which is a hex string dump (spaces ok.) A command line tool (osdp-dump) is also available.

A command line tool for calculating secure channel values is provided (osdp-sc-calc.)
# Installation
## Building and Installing
### Installing on Devuan
linux-devuan-samples
etc/sudoers.d/www-user

# Internals
# Standards Conformance
### iec migration

# punchlist

card data
examples
command-samples
ACU-actions
config-samples
file default for transfer
clean up output control codes
tests for operator_confirm
default for keypad?
dump_status
various conformance tests