OSDP Interop Cable

# Notes
1. Picture attached at end of this document as Figure 1.
2. twisted pair ignored due to short length
3. termination resistors ignored due to short length
4. happy to modify cable if someone can show up with a standard to follow.
# Cable Assembly
## Parts List
For convienence we use a 3-pin Molex connector. It's got 3 wires, it's easy to fabricate with a crimp tool you can buy in an electronics parts shop, and you can get the components in kits. We use the Waldom 1625-3PRT kit (brand is Molex.) This is the .062 inch pin format. The point is to show up to an interop event (or a job site) with interoperable connectors. Automotive-grade connectors would also work. (And there's a 2-wire version too so the same tools/parts can make 12 vdc power cables for many panels and readers.)

4x 3pin male molex
4x 3pin female molex
pins for each (assume you will mess up a few, get extras)
20 gauge solid core wire. red, white, black.
## Tools List
pin crimp tool
wire stripper
## Cable Harness Assembly
build 4-drop cable.
note 2 inner drops hav double the wires in the crimp.

cut cable 3x 0.3 meter lengths r,w,b
strip 3/16 inch each
### about pins:
  male pins go in female shell
  female pins go in male shell
### about wiring the connector:
  red - pointy end
  white - middle
  black - square end

  for inner connectors
    insert 2 stripped cables in pin; crimp; insert in shell
  for outer connectors
    insert stripped cable in pin; crimp; insert in shell
## Device Cable Assembly
for pigtails:
  red is tx+
  white is tx-
  black is ground
## Device Power Cable
power cables:
  2-pin
  DUT gets female shell
  red is +12
  black is -12 / ground

# Figure 1 OSDP Interop Cable

# Appendix
## A. Colophon
Part of libosdp.
### Revision History
added specific part numbers for Molex connectors.